## Slide 1
INTRODUCTION

## Slide 2
The Quattro is a 4DCT respiratory motion phantom comprised of a semi-anthropomorphic chest tissue equivalent phantom and a fully programable four-dimensional dynamic motion unit with an independently motorised rotating insert arm and chest wall arm. Equipped with hyper-versatile and customisable software.
DEMAND
INTRODUCTION
Dynamic phantoms are vital for assessing how patient motion and breathing impacts imaging.
This is also particular important in radiotherapy planning to ensure only the intended tissue
is irradiated .

## Slide 3
PROPERTIES
MATERIALS
DEMAND
FEATURES
INTRODUCTION
Dynamic phantoms are vital for assessing how patient motion and breathing impacts imaging.
This is also particularly important in radiotherapy planning to ensure only the intended tissue
is irradiated.
CT Radiotherapy PET

## Slide 4
FEATURES
PROPERTIES
Lung tissue
equivalent
Spine tissue equivalent
Lung insert
cavity
Central dosimetry cavity
DEMAND
Dynamic phantoms are vital for assessing how patient motion and breathing impacts imaging.
This is also particular important in radiotherapy planning to ensure only the intended tissue
is irradiated .
Horizontal and rotational motion phantom insert arm
Vertical motion arm for breathing surrogate motion
programme upload port
power port and lead
start / stop program

## Slide 5
FEATURES
Horizontal and rotational motion phantom insert arm
Vertical motion arm for breathing surrogate motion
ACCESSORIES
MATERIALS
FEATURES
FEATURES
programme upload port
power port and lead
start / stop program

## Slide 6
FEATURES
PROPERTIES
ACCESSORIES
USAGE
Quattro includes the lung inserts:
Simulated tumour – centred (LN330)
Simulated tumour – off-set (LN330)
PET sphere tumour (LN330+PMMA)
Ion chamber dosimetry (LN330+WT1)
TLD dosimetry (WT1)
Film dosimetry (WT1)
Centre inserts:
Water equivalent rod (WT1)
Ion chamber dosimetry (WT1)
SPECIFICATIONS

## Slide 7
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Quattro hardware specifications
Programmable Z-axis motion = 0 – 7.5 cm/s
Distance range / amplitude = 6.0 cm
Typical within ±0.3% of expected timing
Maximal error ±1.4% of expected timing
Maximum bpm at 6.0cm amplitude = 23bpm
At lower settings breath rate maximum = 30bpm
SOFTWARE

## Slide 8
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
SOFTWARE
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Notes: Moving on to software
Comes included
Allow to customise movement to needs or replicate a patient
Dials
sliders

## Slide 9
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
ADVANCED

## Slide 10
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
ADVANCED
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.

## Slide 11
Wave viewer
Here you can see your generated wave which can be exported or saved for future use.
A complicated realistic human like wave could be created for accurate radiotherapy planning.
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
ADVANCED
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
VIEWING

## Slide 12
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
ADVANCED
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
VIEWING
Wave viewer
Here you can see your generated wave which can be exported or saved for future use.
A complicated and realistic human-like wave could be created for accurate radiotherapy planning.
Or a simple wave for repeatable and reliable quality assessment and control testing.

## Slide 13
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
ADVANCED
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
VIEWING
Wave viewer
Here you can see your generated wave which can be exported or saved for future use.
A complicated realistic human like wave could be created for accurate radiotherapy planning.
Or a simple wave for repeatable and reliable quality assessment and control testing.
And anything in-between!

## Slide 14
Wave viewer
Here you can see your generated wave which can be exported or saved for future use.
And anything in-between!
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
ADVANCED
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
VIEWING
Or a simple wave for repeatable and reliable quality assessment and control testing.
USAGE
3DCT tumour insert scan
Motion during imaging has resulted in a geometrically distorted and inaccurate tumour image
4DCT tumour insert scan
This videographic motion imaging gives a geometrically accurate and defined image needed for diagnostic and interventional radiology/radiotherapy.
Quattro in motion…

## Slide 15
Or a simple wave for repeatable and reliable quality assessment and control testing.
And anything in-between!
Wave viewer
Here you can see your generated wave which can be exported or saved for future use.
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
ADVANCED
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
VIEWING
USAGE
Quattro in motion…
3DCT tumour insert scan
Motion during imaging has resulted in a geometrically distorted and inaccurate tumour image.
4DCT tumour insert scan
This videographic motion imaging gives a geometrically accurate and defined image needed for diagnostic and interventional radiology/radiotherapy.

## Slide 16
Or a simple wave for repeatable and reliable quality assessment and control testing.
And anything in-between!
Wave viewer
Here you can see your generated wave which can be exported or saved for future use.
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
ADVANCED
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
VIEWING
USAGE
Quattro in motion…
3DCT tumour insert scan
Motion during imaging has resulted in a geometrically distorted and inaccurate tumour image.
4DCT tumour insert scan
This videographic motion imaging gives a geometrically accurate and defined image needed for diagnostic and interventional radiology/radiotherapy.
medical imaging phantoms

## Slide 17
Or a simple wave for repeatable and reliable quality assessment and control testing.
And anything in-between!
Wave viewer
Here you can see your generated wave which can be exported or saved for future use.
FEATURES
PROPERTIES
ACCESSORIES
SPECIFICATIONS
INSPECTION
Example wave forms
The software also includes a page of preset example wave forms for quick and simple quality assessment testing.
SOFTWARE
Custom file building
Creating a wave form for the Quattro is very customisable with options to choose:
Amplitude (distance)
Amplitude variation
Breaths per minute (cycle frequency)
Rate variation (breath length variation)
Pause probability (likelihood of pause per cycle)
Length of pause
Run time/duration of the programme
ADVANCED
Custom file building
The shape and style of wave form is also definable with wave options such as:
Sine
Triangle
Fast Inhale
Fast Exhale
With realistic human wave forms options:
Even inhale/exhale
Fast inhale/slow exhale
Slow inhale/fast exhale
Even inhale/exhale with pause
Imported wave form
Custom file building: Advanced options
The wave form and motion of the Quattro arms can also be altered through various specialised settings, these include:
Phase shift (between the phantom insert and chest wall arms)
Amplitude factor (increase or decreases the amount the phantom insert arm moves to that of the chest wall arm)
Noise level
Phantom Insert arm rotation angle
Rotation direction
Rotational hysteresis
VIEWING
USAGE
Quattro in motion…
3DCT tumour insert scan
Motion during imaging has resulted in a geometrically distorted and inaccurate tumour image.
4DCT tumour insert scan
This videographic motion imaging gives a geometrically accurate and defined image needed for diagnostic and interventional radiology/radiotherapy.