## Slide 1
SonIQ Uniformity
Ultrasound Phantom
Phantoms for:
X-ray
Mammography
Fluoroscopy
Nuclear Medicine
Radiotherapy
Ultrasound
CT
MRI
Doc 823a 30/01/24

## Slide 2
SonIQ Uniformity
Ultrasound Phantom
The SonIQ Uniformity allows the user to test linear, curvilinear and intra-cavity ultrasound probes for common defects such as damaged transducer elements or cables.
Such defects will produce non-uniformities in a uniform phantom.
FEATURES

## Slide 3
SonIQ Uniformity
Ultrasound Phantom
FEATURES
Linear probe surface
Curvilinear probe surface
Intra-cavity probe hole
PROPERTIES
MATERIALS

## Slide 4
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
MATERIALS
This material is also chemically stable and non-perishable.
The SonIQ Uniformity is made from a strong mechanically durable, tear and
deformation
resistant, and
hyperflexible
material.
Due to the
flexibility the
intra-cavity probe
hole can accommodate a variety of probe sizes.

## Slide 5
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
Speed of Sound
≈1000±50 m/s
Attenuation
1±0.1 dB/cm/MHz
ACCESSORIES

## Slide 6
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
Background Rod Insert
Anechoic Rod Insert
USAGE
*not actual scale*

## Slide 7
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform image with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
For the best results, use settings specifically for assessing uniformity.
Using a shallow focus ensures a small transmit aperture.

## Slide 8
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
For the best results, use settings specifically for assessing uniformity.
Using a shallow focus ensures a small transmit aperture.
This improves the chance of identifying single element dropout.
Modern controls such as compounding and advanced processing should be turned off as they can mask uniformity faults.

## Slide 9
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
For the best results, use settings specifically for assessing uniformity.
Using a shallow focus ensures a small transmit aperture.
This improves the chance of identifying single element dropout.
Modern controls such as compounding and advanced processing should be turned off as they can mask uniformity faults.
Aswell as assessment with the SonIQ Uniformity phantom is important to check for faults elsewhere in the device.
Check the probe cables and mains cables for any damage by running the cable carefully though the thumb, first and second finger.
This should help to identify any cuts, abrasions, twisting, deformation, or stress internal to the cable.
Also check the probe connectors for any physical damage or signs of stress, particularly twisted or misaligned pins, abrasion or corrosion to surface connections.

## Slide 10
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
INSPECTION
Aswell as assessment with the SonIQ Uniformity phantom it is important to check for faults elsewhere in the device.
Check the probe cables and mains cables for any damage by running the cable carefully through the thumb, first and second finger.
This should help to identify any cuts, abrasions, twisting, deformation, or stress internal to the cable.
Also check the probe connectors for any physical damage or signs of stress, particularly twisted or misaligned pins, and abrasion or corrosion to surface connections.
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.

## Slide 11
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
CARE
Aswell as assessment with the SonIQ Uniformity phantom is important to check for faults elsewhere in the device.
Check the probe cables and mains cables for any damage by running the cable carefully though the thumb, first and second finger.
This should help to identify any cuts, abrasions, twisting, deformation, or stress internal to the cable.
Also check the probe connectors for any physical damage or signs of stress, particularly twisted or misaligned pins, abrasion or corrosion to surface connections.
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.

## Slide 12
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
CARE
Aswell as assessment with the SonIQ Uniformity phantom is important to check for faults elsewhere in the device.
Check the probe cables and mains cables for any damage by running the cable carefully though the thumb, first and second finger.
This should help to identify any cuts, abrasions, twisting, deformation, or stress internal to the cable.
Also check the probe connectors for any physical damage or signs of stress, particularly twisted or misaligned pins, abrasion or corrosion to surface connections.
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.

## Slide 13
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
CARE
Aswell as assessment with the SonIQ Uniformity phantom is important to check for faults elsewhere in the device.
Check the probe cables and mains cables for any damage by running the cable carefully though the thumb, first and second finger.
This should help to identify any cuts, abrasions, twisting, deformation, or stress internal to the cable.
Also check the probe connectors for any physical damage or signs of stress, particularly twisted or misaligned pins, abrasion or corrosion to surface connections.
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.

## Slide 14
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
CARE
Aswell as assessment with the SonIQ Uniformity phantom is important to check for faults elsewhere in the device.
Check the probe cables and mains cables for any damage by running the cable carefully though the thumb, first and second finger.
This should help to identify any cuts, abrasions, twisting, deformation, or stress internal to the cable.
Also check the probe connectors for any physical damage or signs of stress, particularly twisted or misaligned pins, abrasion or corrosion to surface connections.
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or a change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.

## Slide 15
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
INSPECTION
CARE
Aswell as assessment with the SonIQ Uniformity phantom is important to check for faults elsewhere in the device.
Check the probe cables and mains cables for any damage by running the cable carefully though the thumb, first and second finger.
This should help to identify any cuts, abrasions, twisting, deformation, or stress internal to the cable.
Also check the probe connectors for any physical damage or signs of stress, particularly twisted or misaligned pins, abrasion or corrosion to surface connections.
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.

## Slide 16
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
CARE
INSPECTION
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.
To clean, transducers should be wiped gently with a non-textured paper towel, taking care not to cause wear to the lens.

## Slide 17
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
CARE
INSPECTION
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.
To clean, transducers should be wiped gently with a non-textured paper towel, taking care not to cause wear to the lens.
Use of a manufacturer-recommended cleaning agent is acceptable. Avoid use of alcohol, such as alcohol wipes, as these can damage the transducer.

## Slide 18
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
CARE
INSPECTION
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.
To clean, transducers should be wiped gently with a non-textured paper towel, taking care not to cause wear to the lens.
Use of a manufacturer-recommended cleaning agent is acceptable. Avoid use of alcohol, such as in alcohol wipes, as these can damage the transducer.
With the proper care, damage to the device is minimised and the device should function as expected during its lifespan, which can be tested on the SonIQ Unifromity.

## Slide 19
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
CARE
INSPECTION
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.
SonIQ Uniformity is made of a stable but chemically sensitive tissue equivalent material.

## Slide 20
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
CARE
INSPECTION
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.
SonIQ Uniformity is made of a stable but chemically sensitive tissue equivalent material.
Ensure to use a manufacturer recommended cleaning agent, to avoid deterioration of the phantom.

## Slide 21
SonIQ Uniformity
Ultrasound Phantom
FEATURES
PROPERTIES
ACCESSORIES
USAGE
The SonIQ Uniformity should give a perfectly uniform with the standard scattering. Any shadows or streaks indicate defective transducer elements or cables.
CARE
INSPECTION
Inspect all transducers for signs of wear and damage.
Applying light pressure to the probe at the junction between the lens and plastic casing may reveal movement suggesting damage to the bonding.
Abrasive wear may show itself as either a dulling or shining or change in texture of the lens and is most common at one or more of the corners, sometimes demonstrating complete wearing of the lens allowing ultrasound elements to be seen.
The hard plastic casing should also be inspected for hairline cracks.
SonIQ Uniformity is made of a stable but chemically sensitive tissue equivalent material.
Ensure to use a manufacturer recommended cleaning agent, to avoid deterioration of the phantom.
Remove ultrasound gel using soft tissues or skin safe wet wipes and water. Avoid acidic, basic, alcoholic, or chlorine-based cleaning agents.

## Slide 22
SonIQ Uniformity
Ultrasound Phantom
Phantoms for:
X-ray
Mammography
Fluoroscopy
Nuclear Medicine
Radiotherapy
Ultrasound
CT
MRI
Doc 823a 30/01/24